## Slide 1: ACT475x GUI Rev1.0 Guidelines
August 2018

## Slide 2: Basic window
This icon show a dongle is connected to PC
Click “Read” button to acquire the all setting of the powered ACT475x IC on EVK
Click “Write” button to write new setting to the powered ACT475x IC on EVK
Click the drop boxes to select the available option
Click this button to set Main Buck to VCM mode
Click this button to set Main Buck to COT mode

## Slide 3: Advanced Screen
Click “Advance Mode” button to be able to change each bit or register
Click the button to flip the bit value
Right click at the bit button to be able to read or write only the corresponding register
Move this side bar down/up to show other registers